## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #19
Sequential Logic

## Slide 2: Questions?
Scan and ask your questions here! (May be obscured in some slides)
Ask at
https://sets.netlify.app/module/676ca3a07d7f5ffc1741dc65
OR

## Slide 3: Lecture #19: Sequential Logic (1/2)
Introduction
Memory Elements
Latches
3.1 S-R Latch
3.2 D Latch
Flip-flops
4.1 S-R Flip-flop
4.2 D Flip-flop
4.3 J-K Flip-flop
4.4 T Flip-flop

## Slide 4: Lecture #19: Sequential Logic (2/2)
Asynchronous Inputs
Synchronous Sequential Circuit
6.1 Flip-flop Characteristic Tables
6.2 Analysis
6.3 Flip-flop Excitation Tables
6.4 Design
Memory
7.1 Memory Unit
7.2 Read/Write Operations
7.3 Memory Cell
7.4 Memory Arrays

## Slide 5: 1. Introduction (1/2)
Two classes of logic circuits
  Combinational
  Sequential
Combinational Circuit
  Each output depends entirely on the immediate (present) inputs.
Combinational
Logic
: :
inputs
outputs
: :
Sequential Circuit
  Each output depends on both present inputs and state.
Memory
Combinational
Logic
: :
inputs
outputs
: :

## Slide 6: 1. Introduction (2/2)
Two types of sequential circuits:
  Synchronous: outputs change only at specific time
  Asynchronous: outputs change at any time
Multivibrator: a class of sequential circuits
  Bistable (2 stable states)
  Monostable or one-shot (1 stable state)
  Astable (no stable state)
Bistable logic devices
  Latches and flip-flops.
  They differ in the methods used for changing their state.

## Slide 7: 2. Memory Elements (1/3)
Memory element: a device which can remember value indefinitely, or change value on command from its inputs.
command
Memory element
stored value
Q
Characteristic table:
Q(t) or Q: current state
Q(t+1) or Q+: next state

## Slide 8: 2. Memory Elements (2/3)
Memory element with clock.
Clock is usually a square wave.
command
Memory element
stored value
Q
clock
Positive edges
Negative edges
Positive pulses

## Slide 9: 2. Memory Elements (3/3)
Two types of triggering/activation
  Pulse-triggered
  Edge-triggered
Pulse-triggered
  Latches
  ON = 1, OFF = 0
Edge-triggered
  Flip-flops
  Positive edge-triggered (ON = from 0 to 1; OFF = other time)
  Negative edge-triggered (ON = from 1 to 0; OFF = other time)
Positive edges
Negative edges
Positive pulses

## Slide 10: 3.1 S-R Latch (1/3)
Two inputs: S and R.
Two complementary outputs: Q and Q'.
  When Q = HIGH, we say latch is in SET state.
  When Q = LOW, we say latch is in RESET state.
For active-high input S-R latch (also known as NOR gate latch)
  R = HIGH and S = LOW  Q becomes LOW (RESET state)
  S = HIGH and R = LOW  Q becomes HIGH (SET state)
  Both R and S are LOW No change in output Q
  Both R and S are HIGH Outputs Q and Q' are both LOW (invalid!)
Drawback: invalid condition exists and must be avoided.

## Slide 11: 3.1 S-R Latch (2/3)
Active-high input S-R latch:
R
S
Q
Q'
1
0
0
1
1
0
0
0
0
1
1
0
0
1
0
0
1
1
0
0
S
R
Q
Q'
Block diagram:

## Slide 12: 3.1 S-R Latch (3/3)
Characteristic table for active-high input S-R latch:
S
R
Q
Q'
Q(t+1) = ?

S + R'∙Q
S∙R = 0

## Slide 13: 3.1 Active-Low S-R Latch
(You may skip this slide.)
What we have seen is active-high input S-R latch.
There are active-low input S-R latches, where NAND gates are used instead. See diagram on the left below.
S
R
Q
Q'
In this case,
  when R=0 and S=1, the latch is reset (i.e. Q becomes 0)
  when R=1 and S=0, the latch is set (i.e. Q becomes 1)
  when S=R=1, it is a no-change command.
  when S=R=0, it is an invalid command.
Sometimes, we use the alternative gate diagram for the NAND gate. See diagram on the right above. (This appears in more complex latches/flip-flops in the later slides.)
S
R
Q
Q'
(Sometimes, the inputs are labelled as S' and R'.)

## Slide 14: 3.1 Gated S-R Latch
S-R latch + enable input (EN) and 2 NAND gates  a gated S-R latch.
S
R
Q
Q'
EN
S
EN
R
Q
Q'
Outputs change (if necessary) only when EN is high.

## Slide 15: 3.2 Gated D Latch (1/2)
Make input R equal to S'  gated D latch.
D latch eliminates the undesirable condition of invalid state in the S-R latch.
D
EN
Q
Q'
D
Q
Q'
EN

## Slide 16: 3.2 Gated D Latch (2/2)
When EN is high,
  D = HIGH  latch is SET
  D = LOW  latch is RESET
Hence when EN is high, Q “follows” the D (data) input.
When EN=1, Q(t+1) = ?

D
Characteristic table:

## Slide 17: 4. Flip-flops (1/2)
Flip-flops are synchronous bistable devices.
Output changes state at a specified point on a triggering input called the clock.
Change state either at the positive (rising) edge, or at the negative (falling) edge of the clock signal.
Positive edges
Negative edges
Clock signal

## Slide 18: 4. Flip-flops (2/2)
S-R flip-flop, D flip-flop, and J-K flip-flop.
Note the “>” symbol at the clock input.
S
C
R
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
Positive edge-triggered flip-flops
S
C
R
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
Negative edge-triggered flip-flops

## Slide 19: 4.1 S-R Flip-flop
S-R flip-flop: On the triggering edge of the clock pulse,
  R = HIGH and S = LOW  Q becomes LOW (RESET state)
  S = HIGH and R = LOW  Q becomes HIGH (SET state)
  Both R and S are LOW No change in output Q
  Both R and S are HIGH Invalid!
X = irrelevant (“don’t care”)
 = clock transition LOW to HIGH
S
C
R
Q
Q'
Characteristic table of positive edge-triggered S-R flip-flop:

## Slide 20: 4.2 D Flip-flop (1/2)
D flip-flop: Single input D (data). On the triggering edge of the clock pulse,
  D = HIGH  Q becomes HIGH (SET state)
  D = LOW  Q becomes LOW (RESET state)
Hence, Q “follows” D at the clock edge.
A positive edge-triggered D flip-flop formed with an S-R flip-flop.
S
C
R
Q
Q'
CLK
D
 = clock transition LOW to HIGH
Convert S-R flip-flop into a D flip-flop: add an inverter.

## Slide 21: 4.2 D Flip-flop (2/2)
Application: Parallel data transfer.
  To transfer logic-circuit outputs X, Y, Z to flip-flops Q1, Q2 and Q3 for storage.
* After occurrence of negative-going transition
Q1 = X*
D
CLK
Q
Q'
Q2 = Y*
D
CLK
Q
Q'
Q3 = Z*
D
CLK
Q
Q'
Combinational logic circuit
Transfer
X
Y
Z

## Slide 22: 4.3 J-K Flip-flop (1/2)
J-K flip-flop: Q and Q' are fed back to the pulse-steering NAND gates.
No invalid state.
Include a toggle state
  J = HIGH and K = LOW  Q becomes HIGH (SET state)
  K = HIGH and J = LOW  Q becomes LOW (RESET state)
  Both J and K are LOW No change in output Q
  Both J and K are HIGH Toggle

## Slide 23: 4.3 J-K Flip-flop (2/2)
J-K flip-flop circuit:
J
Q
Q'
CLK
Pulse transition detector
K
Characteristic table:
Q(t+1) = ?
J∙Q' + K'∙Q


## Slide 24: 4.4 T Flip-flop
T flip-flop: Single input version of the J-K flip-flop, formed by tying both inputs together.
Characteristic table:
T
Q
Q'
CLK
Pulse transition detector
J
C
K
Q
Q'
CLK
T
Q(t+1) = ?

T∙Q' + T'∙Q

## Slide 25: 5. Asynchronous Inputs (1/2)
S-R, D and J-K inputs are synchronous inputs, as data on these inputs are transferred to the flip-flop’s output only on the triggered edge of the clock pulse.
Asynchronous inputs affect the state of the flip-flop independent of the clock; example: preset (PRE) and clear (CLR) [or direct set (SD) and direct reset (RD)].
When PRE=HIGH, Q is immediately set to HIGH.
When CLR=HIGH, Q is immediately cleared to LOW.
Flip-flop in normal operation mode when both PRE and CLR are LOW.

## Slide 26: 5. Asynchronous Inputs (2/2)
A J-K flip-flop with active-low PRESET and CLEAR asynchronous inputs.
J
Q
Q'
CLK
Pulse transition detector
K
PRE
CLR
J
C
K
Q
Q'
PRE
CLR
PRE
CLR
CLK
Q
Preset
Toggle
Clear
J = K = HIGH

## Slide 27: End of File