## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
Lecture #17
Combinational Circuits

## Slide 2: Questions?
Scan and ask your questions here! (May be obscured in some slides)
Ask at
https://sets.netlify.app/module/676ca3a07d7f5ffc1741dc65
OR

## Slide 3: Lecture #17: Combinational Circuits
Introduction
Analysis Procedure
Design Methods
Gate-Level (SSI) Design
Block-Level Design
Summary of Arithmetic Circuits
Example: 6-Person Voting System
Magnitude Comparator
Circuit Delays

## Slide 4: 1. Introduction
Two classes of logic circuits
  Combinational
  Sequential
Combinational Circuit
  Each output depends entirely on the immediate (present) inputs.
Combinational
Logic
: :
inputs
outputs
: :
Sequential Circuit
  Each output depends on both present inputs and state.
Memory
Combinational
Logic
: :
inputs
outputs
: :

## Slide 5: 2. Analysis Procedure
Given a combinational circuit, how do you analyze its function?
Steps:
  1. Label the inputs and outputs.
AB
F1
F2
A+B
A'+B'
= (A+B).(A'+B')
= (A'+B')' = AB
  2. Obtain the functions of intermediate points and the outputs.
  3. Draw the truth table.
  4. Deduce the functionality of the circuit 
A | B | (A+B) | (A'+B') | F1 | F2
0 | 0 | 0 | 1 | 0 | 0
0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1 | 0
1 | 1 | 1 | 0 | 0 | 1
  Half adder.
What is this circuit?


## Slide 6: 3. Design Methods
Different combinational circuit design methods:
  Gate-level design method (with logic gates)
  Block-level design method (with functional blocks)
Design methods make use of logic gates and useful function blocks
  These are available as Integrated Circuit (IC) chips.
  Types of IC chips (based on packing density): SSI, MSI, LSI, VLSI, ULSI.
Main objectives of circuit design:
  Reduce cost (number of gates for small circuits; number of IC packages for complex circuits)
  Increase speed
  Design simplicity (re-use blocks where possible)

## Slide 7: 4. Gate-Level (SSI) Design: Half Adder (1/2)
Design procedure:
  1. State problem Example: Build a Half Adder.
  2. Determine and label the inputs and outputs of circuit. Example: Two inputs and two outputs labelled, as shown below.
  3. Draw the truth table.
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
X
Y
S
C
(X + Y)
Half
Adder


## Slide 8: 4. Gate-Level (SSI) Design: Half Adder (2/2)
  4. Obtain simplified Boolean functions. Example: C = XY S = X'Y + XY' = XY
  5. Draw the logic diagram.
X | Y | C | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
X
Y
S
C
Half Adder
X
Y
S
C
(X + Y)
Half
Adder

Block diagram of Half Adder

## Slide 9: 4. Gate-Level (SSI) Design: Full Adder (1/5)
Half adder adds up only two bits.
To add two binary numbers, we need to add 3 bits (including the carry).
  Example:
Need Full Adder (so called as it can be made from two half adders).
X
Y
Z
S
C
(X + Y + Z)
Full
Adder


## Slide 10: 4. Gate-Level (SSI) Design: Full Adder (2/5)
Truth table:
Using K-map, simplified SOP form:
  C = XY + XZ + YZ S = X'Y'Z + X'YZ' + XY'Z' + XYZ
Note:
Z - carry in (to the current position)
C - carry out (to the next position)
X | Y | Z | C | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

0
1
00 01 11 10
X
YZ
1
1
1
1
C
0
0
0
0
0
1
00 01 11 10
X
YZ
1
1
1
1
S
0
0
0
0

## Slide 11: 4. Gate-Level (SSI) Design: Full Adder (3/5)
Alternative formulae using algebraic manipulation:
  C = XY + XZ + YZ = XY + (X + Y)Z = XY + ( (XY) + XY )Z = XY + (XY)Z + XYZ = XY + (XY)Z
  S = X'Y'Z + X'YZ' + XY'Z' + XYZ = X'(Y'Z + YZ') + X(Y'Z' + YZ) = X'(YZ) + X(YZ)' = X(YZ)

## Slide 12: 4. Gate-Level (SSI) Design: Full Adder (4/5)
Circuit for above formulae:
  C = XY + (XY)Z
  S = X(YZ) = (XY)Z (XOR is associative)
Full Adder made from two Half-Adders (+ an OR gate).
(XY)
X
Y
S
C
Z
(XY)

## Slide 13: 4. Gate-Level (SSI) Design: Full Adder (5/5)
Circuit for above formulae:
  C = XY + (XY)Z
  S = X(YZ) = (XY)Z (XOR is associative)
Full Adder made from two Half-Adders (+ an OR gate).
(XY)
X
Y
S
C
Z
(XY)
Half
Adder
Half
Adder
X
Y
X
Y
Sum
Carry
Sum
Carry
Block diagrams

## Slide 14: 4. Gate-Level (SSI) Design: Code Converters
Code converter – takes an input code, translates to its equivalent output code.
Code
converter
Input
code
Output
code
Example: BCD to Excess-3 code converter.
  Input: BCD code
  Output: Excess-3 code

## Slide 15: 4. BCD to Excess-3 Code Converter (1/3)
Digit | BCD code | Excess-3 code
0 | 0000 | 0011
1 | 0001 | 0100
2 | 0010 | 0101
3 | 0011 | 0110
4 | 0100 | 0111
5 | 0101 | 1000
6 | 0110 | 1001
7 | 0111 | 1010
8 | 1000 | 1011
9 | 1001 | 1100

## Slide 16: 4. BCD to Excess-3 Code Converter (2/3)
Truth table:
 | BCD |  |  |  | Excess-3 |  |  | 
 | A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
6 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
10 | 1 | 0 | 1 | 0 | X | X | X | X
11 | 1 | 0 | 1 | 1 | X | X | X | X
12 | 1 | 1 | 0 | 0 | X | X | X | X
13 | 1 | 1 | 0 | 1 | X | X | X | X
14 | 1 | 1 | 1 | 0 | X | X | X | X
15 | 1 | 1 | 1 | 1 | X | X | X | X
K-maps:
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
W
0
0
0
0
0
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
X
0
0
0
0
0
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
Y
0
0
0
0
0
1
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
Z
0
0
0
0
0

## Slide 17: 4. BCD to Excess-3 Code Converter (3/3)
1
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
Z
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
W
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
X
A
C
00
01
11
10
00 01 11 10
D
AB
CD
B
X
X
X
X
X
X
1
1
1
1
1
Y
W = A + BC + BD
X = B'C + B'D + BC'D'
Y = C.D + C'.D'
Z = D'


## Slide 18: 5. Block-Level Design
More complex circuits can also be built using block-level method.
In general, block-level design method (as opposed to gate-level design) relies on algorithms or formulae of the circuit, which are obtained by decomposing the main problem to sub-problems recursively (until small enough to be directly solved by blocks of circuits).
First example shows how to create a 4-bit parallel adder using block-level design.
Using 4-bit parallel adders as building blocks, we can create the following:
  1. BCD-to-Excess-3 Code Converter
  2. 16-bit Parallel Adder

## Slide 19: 5. 4-bit Parallel Adder (1/4)
Consider a circuit to add two 4-bit numbers together and a carry-in, to produce a 5-bit result.
4-bit
Parallel Adder
C5
C1
X2
X1
Y4
Y3
S4
S3
S2
S1
Y2
Y1
X4
X3
Black-box view of 4-bit parallel adder
5-bit result is sufficient because the largest result is: 11112 + 11112 + 12 = 111112

## Slide 20: 5. 4-bit Parallel Adder (2/4)
SSI design (gate-level design) technique should not be used here.
Truth table for 9 inputs is too big: 29 = 512 rows!
Simplification becomes too complicated!
X4X3X2X1 | Y4Y3Y2Y1 | C1 | C5 | S4S3S2S1
0 0 0 0 | 0 0 0 0 | 0 | 0 | 0 0 0 0
0 0 0 0 | 0 0 0 0 | 1 | 0 | 0 0 0 1
0 0 0 0 | 0 0 0 1 | 0 | 0 | 0 0 0 1
… | … | … | … | …
0 1 0 1 | 1 1 0 1 | 1 | 1 | 0 0 1 1
… | … | … | … | …
1 1 1 1 | 1 1 1 1 | 1 | 1 | 1 1 1 1

## Slide 21: 5. 4-bit Parallel Adder (3/4)
Alternative design possible.
Addition formula for each pair of bits (with carry in), Ci+1Si = Xi + Yi + Ci has the same function as a full adder: Ci+1 = Xi Yi + (Xi Yi)Ci Si = Xi  Yi  Ci
C =
X = 1 0 1 0
Y = 1 1 1 1
X + Y =
0
1
1
0
1
1
0
0
1

## Slide 22: 5. 4-bit Parallel Adder (4/4)
Cascading 4 full adders via their carries, we get:
C1
Y1 X1
S1
FA
C2
C5
Y2 X2
S2
FA
C3
Y3 X3
S3
FA
C4
Y4 X4
S4
FA
Output
Input
Note that carry is propagated by cascading the carry from one full adder to the next.
Called Parallel Adder because inputs are presented simultaneously (in parallel). Also called Ripple-Carry Adder.

## Slide 23: 5. BCD to Excess-3 Converter: Revisit (1/2)
Excess-3 code can be converted from BCD code using truth table:
 | BCD |  |  |  | Excess-3 |  |  | 
 | A | B | C | D | W | X | Y | Z
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1
1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0
2 | 0 | 0 | 1 | 0 | 0 | 1 | 0 | 1
3 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
4 | 0 | 1 | 0 | 0 | 0 | 1 | 1 | 1
5 | 0 | 1 | 0 | 1 | 1 | 0 | 0 | 0
6 | 0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
7 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 0
8 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1
9 | 1 | 0 | 0 | 1 | 1 | 1 | 0 | 0
10 | 1 | 0 | 1 | 0 | X | X | X | X
11 | 1 | 0 | 1 | 1 | X | X | X | X
12 | 1 | 1 | 0 | 0 | X | X | X | X
13 | 1 | 1 | 0 | 1 | X | X | X | X
14 | 1 | 1 | 1 | 0 | X | X | X | X
15 | 1 | 1 | 1 | 1 | X | X | X | X
Gate-level design can be used since only 4 inputs.
However, alternative design is possible.
Use problem-specific formula:
  Excess-3 code = BCD Code + 00112

## Slide 24: 5. BCD to Excess-3 Converter: Revisit (2/2)
Block-level circuit:
4-bit Parallel Adder
X4
X3
X2
X1
Y4
Y3
Y2
Y1
0
0
1
1
S4
S3
S2
S1
BCD
code
Excess-3
code
unused
0
Cin
Cout
A BCD to Excess-3 Code Converter
Note: In the lab, input 0 (low) is connected to GND, 1 (high) to Vcc.

## Slide 25: 5. 16-bit Parallel Adder
Larger parallel adders can be built from smaller ones.
Example: A 16-bit parallel adder can be constructed from four 4-bit parallel adders:
4-bit // adder
X4..X1
Y4..Y1
C1
S4..S1
4-bit // adder
X8..X5
Y8..Y5
C5
S8..S5
4-bit // adder
X12..X9
Y12..Y9
C9
S12..S9
4-bit // adder
X16..X13
Y16..Y13
C13
S16..S13
C17
4
4
4
4
4
4
4
4
4
4
4
4
A 16-bit parallel adder
4
S4..S1
S4S3S2S1
=

## Slide 26: 6. Summary of Arithmetic Circuits (1/4)
Half adder
X
Y
S
C
S
Input bits
Output bits
x
y'
S = xy' + x'y
x'
y
x
y
C
x
y
S = (x+y)(x'+y')
x'
y'
x
y
C
x'
y'
S = (C+x'y')'
x
y
C
x
y
C
S = x  y

## Slide 27: 6. Summary of Arithmetic Circuits (2/4)
Full adder
Input bits
Output bits
A
B
S
Cout
S
Cin
0
1
00 01 11 10
x
yz
C = xy + xz + yz
1
1
1
1
1
S = x'y'z + x'yz' + xy'z' + xyz
0
1
00 01 11 10
x
yz
1
1
1
x
y
S = (xy)z
C = xy + (xy)z
z
xy
xy
X'
y'
z
S
x'
y
z'
x
y'
z'
x
y
z
C
x
z
y
z
x
y

## Slide 28: 6. Summary of Arithmetic Circuits (3/4)
4-bit parallel adder
2 ways:
  Serial (one FA)
  Parallel (n FAs for n bits)
C1
Y1 X1
S1
C2
C5
Y2 X2
S2
C3
Y3 X3
S3
C4
Y4 X4
S4
FA
FA
FA
FA
X
Y
S
Cout
S
Cin
Input carry
Binary no. B
Binary no. A
Output carry
4-bit sum

## Slide 29: 6. Summary of Arithmetic Circuits (4/4)
Cascading 4 full adders (FAs) gives a 4-bit parallel adder.
  Classical method: 9 input variables  29 = 512 rows in truth table!
Cascading method can be extended to larger adders.
  Example: 16-bit parallel adder.
4-bit // adder
X4..X1
Y4..Y1
C1
S4..S1
4-bit // adder
X8..X5
Y8..Y5
C5
S8..S5
4-bit // adder
X12..X9
Y12..Y9
C9
S12..S9
4-bit // adder
X16..X13
Y16..Y13
C13
S16..S13
C17
4
4
4
4
4
4
4
4
4
4
4
4

## Slide 30: 7. Example: 6-Person Voting System
Application: 6-person voting system.
  Use FAs and a 4-bit parallel adder.
  Each FA can sum up to 3 votes.
Voter 1
3-bit Output
A
B
S
Cout
S
Cin
Voter 2
Voter 3
Voter 4
A
B
S
Cout
S
Cin
Voter 5
Voter 6
Full-adder 1
Full-adder 2
S
Cout
Cin
A
1
2
3
4
B
1
2
3
4
S
1
2
3
4
Parallel adder
1
0
1
0
1
0
0
1
1
0
1
1
0
1
1
0
1
1
1
0
1
1
1
1
0
1


## Slide 31: 8. Magnitude Comparator (1/4)
Magnitude comparator: compares 2 unsigned values A and B, to check if A>B, A=B, or A<B.
To design an n-bit magnitude comparator using classical method, it would require 22n rows in truth table!
We shall exploit regularity in our design.
Question: How do we compare two 4-bit unsigned values A (a3a2a1a0) and B (b3b2b1b0)?
  If (a3 > b3) then A > B
  If (a3 < b3) then A < B
  If (a3 = b3) then if (a2 > b2) …

## Slide 32: 8. Magnitude Comparator (2/4)
Let A = A3A2A1A0 , B = B3B2B1B0; xi = AiBi + Ai'Bi'
A2
B2
A3
B3
A0
B0
A1
B1
(A < B)
(A > B)
(A = B)
x3
x2
x1
x0
A3'B3
A3B3'
A3'B3 + x3A2'B2
+ x3x2.A1'B1
+ x3x2x1A0'B0
A3B3' + x3A2B2'
+ x3x2A1B1'
+ x3x2x1A0B0'
x3x2x1x0


## Slide 33: 8. Magnitude Comparator (3/4)
Block diagram of a 4-bit magnitude comparator
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
0
1
1
0
1
0
1
0
1
0
0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
0
1
1
0
0
0
1
1
0
1
0

## Slide 34: 8. Magnitude Comparator (4/4)

A function F accepts a 4-bit binary value ABCD, and returns 1 if 3  ABCD  12, or 0 otherwise. How would you implement F using magnitude comparators and a suitable logic gate?
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A3
A2
A1
A0
4-bit Comp
(A < B)
(A > B)
(A = B)
B3
B2
B1
B0
A
B
C
D
0
0
1
0
1
1
0
1
F

## Slide 35: 9. Circuit Delays (1/5)
Given a logic gate with delay t. If inputs are stable at times t1, t2, …, tn, then the earliest time in which the output will be stable is: max( t1, t2, …, tn ) + t
t1
Logic
Gate
t2
tn
:
:
max (t1, t2, ..., tn ) + t
To calculate the delays of all outputs of a combinational circuit, repeat above rule for all gates.

## Slide 36: 9. Circuit Delays (2/5)
As a simple example, consider the full adder circuit where all inputs are available at time 0. Assume each gate has delay t.
Outputs S and C experience delays of 2t and 3t respectively.
max(0,0)+t = t
t
X
Y
S
C
Z
0
0
0
max(t,0)+t = 2t
max(t,2t)+t = 3t
2t

## Slide 37: 9. Circuit Delays (3/5)
More complex example: 4-bit parallel adder.
C1
Y1 X1
S1
FA
C2
C5
Y2 X2
S2
FA
C3
Y3 X3
S3
FA
C4
Y4 X4
S4
FA
0
0
0
0
0
0
0
0
0

## Slide 38: 9. Circuit Delays (4/5)
Analyse the delay for the repeated block.
where Xi, Yi are stable at 0t, while Ci is assumed to be stable at mt.
Full
Adder
Xi
Yi
Ci
Si
Ci+1
0
0
mt
Performing the delay calculation:
Xi
Yi
Si
Ci+1
Ci
max(0,0)+t = t
t
0
0
mt
max(t,mt)+t
max(t,mt)+2t
max(t,mt)+t

## Slide 39: 9. Circuit Delays (5/5)
Calculating:
  When i=1, m=0; S1 = 2t and C2 = 3t
  When i=2, m=3; S2 = 4t and C3 = 5t
  When i=3, m=5; S3 = 6t and C4 = 7t
  When i=4, m=7; S4 = 8t and C5 = 9t
In general, an n-bit ripple-carry parallel adder will experience the following delay times:
  Sn = ( (n – 1)2 + 2 ) t
  Cn+1 = ( (n – 1)2 + 3 ) t
Propagation delay of ripple-carry parallel adders is proportional to the number of bits it handles.
Maximum delay: ( (n – 1)2 + 3 ) t
Full
Adder
Xi
Yi
Ci
Si
Ci+1
0
0
mt
max(t,mt)+t
max(t,mt)+2t

## Slide 40: Quick Review Questions
DLD pages 128 – 129 Questions 6-1 to 6-4.

## Slide 41: End of File