## Slide 1: http://www.comp.nus.edu.sg/~cs2100/
CS2100
Recitation 10
Sequential Circuits
31 March 2025
(Make-up on 27 March 2025)
Aaron Tan

## Slide 2: Contents
Latches
Flip-flops
Analysis of Sequential Circuits
Design of Sequential Circuits
Quizzes
Selected Past Years’ Exam Questions
  AY2015/16 Sem1 Q7
  AY2020/21 Sem2 Q12

## Slide 3: 1. Introduction
Two classes of logic circuits
  Combinational
  Sequential
Combinational Circuit
  Each output depends entirely on the immediate (present) inputs.
Combinational
Logic
: :
inputs
outputs
: :
Sequential Circuit
  Each output depends on both present inputs and state.
Memory
Combinational
Logic
: :
inputs
outputs
: :
2 weeks ago…

## Slide 5: summary
Latches

## Slide 6: 3.1 S-R Latch (2/3)
Active-high input S-R latch:
R
S
Q
Q'
1
0
0
1
1
0
0
0
0
1
1
0
0
1
0
0
1
1
0
0
S
R
Q
Q'
Block diagram:
Characteristic table:
Key: When tracing a lach/flip-flop, do it 3 rounds.

## Slide 7: 3.1 Active-Low S-R Latch
(You may skip this slide.)
What we have seen is active-high input S-R latch.
There are active-low input S-R latches, where NAND gates are used instead. See diagram on the left below.
S
R
Q
Q'
In this case,
  when R=0 and S=1, the latch is reset (i.e. Q becomes 0)
  when R=1 and S=0, the latch is set (i.e. Q becomes 1)
  when S=R=1, it is a no-change command.
  when S=R=0, it is an invalid command.
Sometimes, we use the alternative gate diagram for the NAND gate. See diagram on the right above. (This appears in more complex latches/flip-flops in the later slides.)
S
R
Q
Q'
(Sometimes, the inputs are labelled as S' and R'.)

## Slide 8: 3.1 Active-High vs Active-Low S-R Latch
R
S
Q
Q'
(Active-high) S-R latch
Active-low S-R latch
S | R | Q(t+1) | Command
0 | 0 | Q(t) | No change
0 | 1 | 0 | Reset
1 | 0 | 1 | Set
1 | 1 | ? | Invalid
S | R | Q(t+1) | Command
1 | 1 | Q(t) | No change
1 | 0 | 0 | Reset
0 | 1 | 1 | Set
0 | 0 | ? | Invalid
S
R
Q
Q'

## Slide 9: 3.1 Gated S-R Latch
S-R latch + enable input (EN) and 2 NAND gates  a gated S-R latch.
S
R
Q
Q'
EN
S
EN
R
Q
Q'
Outputs change (if necessary) only when EN is high.
Characteristic table:
EN | S | R | Q(t+1) | Command
1 | 0 | 0 | Q(t) | No change
1 | 0 | 1 | 0 | Reset
1 | 1 | 0 | 1 | Set
1 | 1 | 1 | ? | Invalid
0 | X | X | Q(t) | 

## Slide 10: 3.2 Gated D Latch (1/2)
Make input R equal to S'  gated D latch.
D latch eliminates the undesirable condition of invalid state in the S-R latch.
D
EN
Q
Q'
D
Q
Q'
EN
Characteristic table:

## Slide 11: summary
Flip-Flops

## Slide 12: 4. Flip-flops (1/2)
Flip-flops are synchronous bistable devices.
Output changes state at a specified point on a triggering input called the clock.
Change state either at the positive (rising) edge, or at the negative (falling) edge of the clock signal.
Positive edges
Negative edges
Clock signal

## Slide 13: 4.1 S-R Flip-flop
S-R flip-flop: On the triggering edge of the clock pulse,
  R = HIGH and S = LOW  Q becomes LOW (RESET state)
  S = HIGH and R = LOW  Q becomes HIGH (SET state)
  Both R and S are LOW No change in output Q
  Both R and S are HIGH Invalid!
X = irrelevant (“don’t care”)
 = clock transition LOW to HIGH
S
C
R
Q
Q'
Characteristic table of positive edge-triggered S-R flip-flop:

## Slide 14: 4.2 D Flip-flop (1/2)
D flip-flop: Single input D (data). On the triggering edge of the clock pulse,
  D = HIGH  Q becomes HIGH (SET state)
  D = LOW  Q becomes LOW (RESET state)
Hence, Q “follows” D at the clock edge.
A positive edge-triggered D flip-flop formed with an S-R flip-flop.
S
C
R
Q
Q'
CLK
D
 = clock transition LOW to HIGH
Convert S-R flip-flop into a D flip-flop: add an inverter.

## Slide 15: 4.3 J-K Flip-flop (2/2)
J-K flip-flop circuit:
J
Q
Q'
CLK
Pulse transition detector
K
Characteristic table:
Q(t+1) = ?
J∙Q' + K'∙Q


## Slide 16: 4.4 T Flip-flop
T flip-flop: Single input version of the J-K flip-flop, formed by tying both inputs together.
Characteristic table:
T
Q
Q'
CLK
Pulse transition detector
J
C
K
Q
Q'
CLK
T
Q(t+1) = ?

T∙Q' + T'∙Q

## Slide 17: 5. Asynchronous Inputs (1/2)
S-R, D and J-K inputs are synchronous inputs, as data on these inputs are transferred to the flip-flop’s output only on the triggered edge of the clock pulse.
Asynchronous inputs affect the state of the flip-flop independent of the clock; example: preset (PRE) and clear (CLR) [or direct set (SD) and direct reset (RD)].
When PRE=HIGH, Q is immediately set to HIGH.
When CLR=HIGH, Q is immediately cleared to LOW.
Flip-flop in normal operation mode when both PRE and CLR are LOW.

## Slide 18: 5. Asynchronous Inputs (2/2)
A J-K flip-flop with active-low PRESET and CLEAR asynchronous inputs.
J
Q
Q'
CLK
Pulse transition detector
K
PRE
CLR
J
C
K
Q
Q'
PRE
CLR
PRE
CLR
CLK
Q
Preset
Toggle
Clear
J = K = HIGH

## Slide 19: COMMON Questions
From previous semester

## Slide 20
Q2: Does Q(t+1), Q+ and Q’ all mean the same thing?
A: Q(t) and Q(t+1) mean present state and next state respectively. They can also be referred to simply as Q and Q+ respectively. So, Q = Q(t), and Q+ = Q(t+1).
Q’ is the complement of Q. Therefore, Q’ is not the same as Q (in fact, it is the negation/opposite of Q), nor is it the same as Q+ (it has no relationship to Q+).
Q1: How does slide 9 of lect 19 work? Why is it that both R and S are high considered an invalid input?
A: It has been illustrated that when both R and S are high, the output Q and Q’ are the same, which violates the definition of a latch/flip-flop.
Q3: L19 slide 10, the outputs are redirected as inputs, and to get outputs we need inputs first. How does the whole thing work as it seems like a never-ending cycle.
A: If there isn’t a clock, will be a “never-ending cycle”. The clock provides synchronisation. The flip flop acts only when it is activated (by the rising edge or falling edge of the clock).

## Slide 21
Q4: Why is there a circle at Q’ output on the flip flop?
A: Just a labelling convention, to remind users that the output (Q’) is the negation of Q.
S
C
R
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
Positive edge-triggered flip-flops
S
C
R
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
Negative edge-triggered flip-flops

## Slide 22
Q5: What do Q and Q’ represent on the flip flop?
S
C
R
Q
Q'
D
C
Q
Q'
J
C
K
Q
Q'
Positive edge-triggered flip-flops
A: Q is the state of the flip-flop and Q’ is the negation of Q.
A flip-flop is a one-bit memory unit; when it stores a 0 it is said to be in the reset state; when it stores a 1 it is in the set state. The Q output of a flip-flop determines the state it is in.

## Slide 23
Analysis
Design
Just for illustration. The state diagram here does not correspond to the logic circuit.
Uses flip-flop characteristic tables.
Uses flip-flop excitation tables.
Logic circuit
State diagram

## Slide 24: summary
Analysis of Sequential Circuits

## Slide 25: 6.1 Flip-flop Characteristic Tables
Each type of flip-flop has its own behaviour, shown by its characteristic table.

## Slide 26: 6.2 Analysis: Example #2 (1/3)
Given Figure 2, a sequential circuit with two J-K flip-flops A and B, and one input x.
Obtain the flip-flop input functions from the circuit:
  JA = B JB = x'
  KA = B∙x' KB = A'∙x + A∙x' = A  x
A
B
x
CP
J
Q
Q'
K
J
Q
Q'
K
Figure 2

## Slide 27: 6.2 Analysis: Example #2 (2/3)
  JA = B JB = x'
  KA = B∙x' KB = A'∙x + A∙x' = A  x
Fill the state table using the above functions, knowing the characteristics of the flip-flops used.
0 1
0 0
1 1
1 0
1 1
1 0
0 0
1 1


## Slide 28: 6.2 Analysis: Example #2 (3/3)
Draw the state diagram from the state table.
00
01
10
11
1
0
1
0
0
1
0
1


## Slide 29: summary
Design of Sequential Circuits

## Slide 30: 6.3 Flip-flop Excitation Tables (1/2)
Excitation tables: given the required transition from present state to next state, determine the flip-flop input(s).
JK Flip-flop
SR Flip-flop
D Flip-flop
T Flip-flop

## Slide 31: 6.4 Design: Example #1 (1/5)

Given the following state diagram, design the sequential circuit using JK flip-flops.
00
10
11
0
0
0
0
1
1
1
1
01
Questions:
How many flip-flops are needed?
How many input variable are there?
Answers:
Two flip-flops. Let’s call them A and B.
One input variable. Let’s call it x.

## Slide 32: 6.4 Design: Example #1 (2/5)

Circuit state/excitation table, using JK flip-flops.
00
10
11
0
0
0
0
1
1
1
1
01
JK Flip-flop’s
excitation table.
0 X
0 X
1 X
0 X
X 0
X 0
X 0
X 1
0 X
1 X
X 1
X 0
0 X
1 X
X 0
X 1

## Slide 33: 6.4 Design: Example #1 (3/5)
Block diagram.
What are to go in here?
Combinational
circuit
A'
A
B
B'
x
KA
JA
KB
JB
B
B'
A
A'
External
input(s)
CP
External
output(s)
(none)
J
Q
Q'
K
J
Q
Q'
K

## Slide 34: 6.4 Design: Example #1 (4/5)
From state table, get flip-flop input functions.
A
B
0
1
00 01 11 10
x
A
Bx
X
X
X
X
1
JA = B∙x'
JB = x
A
B
0
1
00 01 11 10
x
A
Bx
X
1
X
X
X
1
KA = B∙x
A
B
0
1
00 01 11 10
x
A
Bx
X
1
X
X
X
KB = (A  x)'
A
B
0
1
00 01 11 10
x
A
Bx
X
1
X
1
X
X

## Slide 35: 6.4 Design: Example #1 (5/5)
Flip-flop input functions:
  JA = B∙x' JB = x
  KA = B∙x KB = (A  x)'
Logic diagram:
x
B
A
CP
J
Q
Q'
K
J
Q
Q'
K

## Slide 36: 6.4 Design: Example #3 (1/4)
Design involving unused states.
Given these
Derive these
Unused state 000:
Are there other unused states?

## Slide 37: 6.4 Design: Example #3 (2/4)
From state table, obtain expressions for flip-flop inputs.
SA = B∙x
RA = C∙x'
SB = A'∙B'∙x
RB = B∙C + B∙x
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
1
B
X
X
X
X
X
X
X
X
X
0
0
0
0
0
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
B
X
X
X
X
X
X
X
X
X
X
0
0
0
0
0
B
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
X
X
X
X
X
X
X
0
0
0
0
0
0
0
0
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
B
X
X
X
1
X
X
X
X
1
X
X
X
X
1
0
0

## Slide 38: 6.4 Design: Example #3 (3/4)
From state table, obtain expressions for flip-flop inputs (cont’d).
SC = x'
RC = x
y = A∙x
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
1
B
X
X
X
X
X
X
X
X
X
0
0
0
0
0
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
B
X
X
1
X
X
X
X
1
X
X
0
0
0
0
0
B
A
C
00
01
11
10
00 01 11 10
x
AB
Cx
1
X
X
X
X
X
X
1
0
0
0
0
0
0
0
0

## Slide 39: 6.4 Design: Example #3 (4/4)
From derived expressions, draw the logic diagram:
SA = B∙x SB = A'∙B'∙x SC = x' y = A∙x
RA = C∙x' RB = B∙C + B∙x RC = x
A
A'
B
B'
y
CP
x
S
Q
Q'
R
S
Q
Q'
R
S
Q
Q'
R
C

## Slide 40: Self-Correcting Circuits (1/4)
When a circuit has unused states, these unused states are considered to be “invalid”.
Suppose we have a circuit with 2 flip-flops where states 0 to 2 are used. State 3 is unused and considered to be “invalid”.
On the following pages we see two possible state diagrams for this circuit.

## Slide 41: Self-Correcting Circuits (2/4)
Case 1: Non-self-correcting Circuit:
  If the circuit finds itself in state 3 (e.g. due to a glitch), it will never transit into a valid state (state 0, 1, or 2).
0
00
01
10
11
0
1
0
1
1
0,1
Case 2: Self-Correcting Circuit
  A circuit that will (eventually) find its way back to a valid state.
  Here even if the circuit finds itself in state 3, it will transit to a valid state (either state 1 or 2)
0
00
01
10
11
0
1
0
1
1
0
1

## Slide 42: Self-Correcting Circuits (3/4)
Is Design Example #3 self-correcting?
  We recreate the state table for the invalid states and see if they lead to any valid states:
Valid states: 1, 2, 3, 4, 5.
Invalid states: 0, 6, 7.

## Slide 43: Self-Correcting Circuits (4/4)
Is Design Example #3 self-correcting?
  The transitions for the invalid states is summarized below:
  We can see that every invalid state eventually transits to some valid state, hence this circuit is self-correcting.
Valid states: 1, 2, 3, 4, 5.
Invalid states: 0, 6, 7.

## Slide 44
QnA Q2:
Some of the tutorial qns require very long truth table + kmap which I feel is almost impossible to draw quickly during exam.
Any tips to be faster?

## Slide 45: QnA Topic 8
From previous semester:
Q7. hi prof, can you go through the memory array portion the 4k x 8 ram portion

## Slide 46: 7.3 Memory Cell
R
S
Q
Input
Select
Output
Read/Write
BC
Output
Input
Select
Read/Write
Logic diagram
Block diagram
A single memory cell of the static RAM has the following logic and block diagrams:

## Slide 47: 7.4 Memory Arrays (3/4)
1K x 8
DATA (8)
ADRS (10)
CS
RW
Read/write
(8)
Output data
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
0–1023
1024 – 2047
2048 – 3071
3072 – 4095
Input data
8 lines
0
1
2
3
2x4 decoder
Lines
Lines
0 – 9
11 10
S0
S1
Address
1K x 8
DATA (8)
ADRS (10)
CS
RW
(8)
Output data
8 lines
Input data
8 lines
Enable
Read/write
Address
10 lines
1K x 8bits RAM
Building a 4K x 8bits RAM using 1K x 8bits RAMs.
4K locations 12-bit address.

## Slide 48: 7.4 Memory Arrays (4/4)
2M  32 memory module
  Using 512K  8 memory chips.
Chip select
512K x 8 memory chip
19-bit
address
8-bit data
input/output
19-bit internal chip address
2-bit
decoder
addresses
21-bit
A
0
A
1
A
19
512k X 8
memory chip
A
20
D
31-24
D
7-0
D
23-16
D
15-8
Read/write control line not included in this diagram.

## Slide 49: Past YEARs’ QUESTIONS
Sequential Circuits
AY2015/16 Sem1 Q7
AY2020/21 Sem2 Q12

## Slide 50: AY2015/16 Sem1 Q7

## Slide 51: AY2015/16 Sem1 Q7
A | B | C | A+ | B+ | C+ | JA | KA | TB | DC
0 | 0 | 0 | 0 | 0 | 1 |  |  |  | 
0 | 0 | 1 | 0 | 1 | 0 |  |  |  | 
0 | 1 | 0 | 0 | 1 | 1 |  |  |  | 
0 | 1 | 1 | 1 | 0 | 0 |  |  |  | 
1 | 0 | 0 | 1 | 0 | 1 |  |  |  | 
1 | 0 | 1 | 1 | 0 | 1 |  |  |  | 
1 | 1 | 0 |  |  |  |  |  |  | 
1 | 1 | 1 |  |  |  |  |  |  | 
X X X X X X X
X X X X X X X
JK flip-flop excitation table
0 X
0 X
0 X
1 X
X 0
X 0
0
1
0
1
0
0
1
0
1
0
1
1
JA = BC
KA = 0
TB = A'C
DC = A+C'

## Slide 52: AY2015/16 Sem1 Q7
A | B | C | A+ | B+ | C+ | JA | KA | TB | DC
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | 1
0 | 0 | 1 | 0 | 1 | 0 | 0 | X | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | X | 0 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1 | X | 1 | 0
1 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | X | 0 | 0 | 1
1 | 1 | 0 | X | X | X | X | X | X | X
1 | 1 | 1 | X | X | X | X | X | X | X
JA = BC
KA = 0
TB = A'C
DC = A+C'

## Slide 53: AY2015/16 Sem1 Q7
A | B | C | A+ | B+ | C+ | JA | KA | TB | DC
0 | 0 | 0 | 0 | 0 | 1 | 0 | X | 0 | 1
0 | 0 | 1 | 0 | 1 | 0 | 0 | X | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 0 | X | 0 | 1
0 | 1 | 1 | 1 | 0 | 0 | 1 | X | 1 | 0
1 | 0 | 0 | 1 | 0 | 1 | X | 0 | 0 | 1
1 | 0 | 1 | 1 | 0 | 1 | X | 0 | 0 | 1
1 | 1 | 0 | X | X | X | X | X | X | X
1 | 1 | 1 | X | X | X | X | X | X | X
6
7
JA = BC
KA = 0
TB = A'C
DC = A+C'
(0)
(1)
(0)
(0)
(0)
(0)
(1)
(1)
(1)
(1)
(1)
(1)
(1)
(1)
No

## Slide 54: AY2020/21 Sem2 Q12
A | B | C | x | JA | KA | JB | KB | JC | KC | A+ | B+ | C+
0 | 0 | 0 | 0 |  |  |  |  |  |  |  |  | 
0 | 0 | 0 | 1 |  |  |  |  |  |  |  |  | 
0 | 0 | 1 | 0 |  |  |  |  |  |  |  |  | 
0 | 0 | 1 | 1 |  |  |  |  |  |  |  |  | 
0 | 1 | 0 | 0 |  |  |  |  |  |  |  |  | 
0 | 1 | 0 | 1 |  |  |  |  |  |  |  |  | 
0 | 1 | 1 | 0 |  |  |  |  |  |  |  |  | 
0 | 1 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 | 0 | 0 | 0 |  |  |  |  |  |  |  |  | 
1 | 0 | 0 | 1 |  |  |  |  |  |  |  |  | 
1 | 0 | 1 | 0 |  |  |  |  |  |  |  |  | 
1 | 0 | 1 | 1 |  |  |  |  |  |  |  |  | 
1 | 1 | 0 | 0 |  |  |  |  |  |  |  |  | 
1 | 1 | 0 | 1 |  |  |  |  |  |  |  |  | 
1 | 1 | 1 | 0 |  |  |  |  |  |  |  |  | 
1 | 1 | 1 | 1 |  |  |  |  |  |  |  |  | 
JA = Ax
KA = B
JB = x’
KB = C’
JC = x’
KC = 1
Ax
B
x’
C’
x’
1
0
0
0
0
0
0
0
0
0
1
0
1
0
1
0
1
0
0
0
0
1
1
1
1
0
0
0
0
1
1
1
1
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1
0
0
1
1
0
0
1
1
0
0
1
1
0
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
0
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
0
0
0
0
0
0
0
0
1
1
1
1
0
0
0
0
1
0
1
0
0
0
1
1
1
0
1
0
0
0
1
1
1
0
0
0
1
0
0
0
1
0
0
0
1
0
0
0
0
1
0
1
0
1
0,1

## Slide 55: AY2020/21 Sem2 Q12
A | B | C | x | JA | KA | JB | KB | JC | KC | A+ | B+ | C+
0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 0 | 1 | 1
0 | 0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 1 | 1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1 | 0 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0
1 | 1 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1 | 0 | 1 | 0 | 0 | 0
1 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0
1
0
1
0
1
0,1
JA = Ax
KA = B
JB = x’
KB = C’
JC = x’
KC = 1

## Slide 56: AY2020/21 Sem2 Q12
F | G | x | F+ | G+
0 | 0 | 0 | 1 | 1
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0
0
1
0
1
0
1
0,1
Note that Q+ = D for D flip-flops.
So F+ = DF and G+ = DG.
x
F
G
DF
1
0
0
1
0
0
1
1
x
F
G
DG
1
0
0
0
1
0
0
0
DF = F’x’ + FG
DG = G’x’

## Slide 57: End of File